## Slide 1: ZTA 24:04 CREATION OF A NEW SOLAR DISTRICT AND ADDING SUPPLEMENTAL REGULATIONS FOR UTILITY SCALE SOLAR GENERATION FACILITIES
Dan Whitten, County Attorney
September 10, 2024
A great place to live, learn, work, and play!

## Slide 2: Removal of Utility Scale Solar in A-1
At the Board of Supervisors’ meeting on July 3, the Board approved the amendment to§22-4-2.2 of the Fluvanna County Code to remove utility scale solar generation facilities as a use allowed by special use permit in the Agricultural, A-1 Zoning District.

## Slide 3: Creation of new County-wide S-1 District
The Solar Ordinance Review Committee has been working on a new proposed zoning district, S-1.
The Committee discussed keeping the proposed S-1 district within a certain distance from transmission lines, but ultimately decided to make it available as an option for rezoning County-wide.

## Slide 4: Creation of new County-wide S-1 District
S-1 keeps the following by-right A-1 uses: agriculture, conservation areas, farm sales, accessory uses, non-commercial cemeteries, non-commercial greenhouses, small-scale solar generating facilities, and minor utilities.
S-1 keeps the following SUP-only A-1 uses: agricultural enterprise, wholesale agricultural sales, commercial livestock feed lots and sales yards, communications services, minor-scale solar generating facilities, telecommunication facilities, and major utilities.
S-1 adds utility-scale solar generating facilities as use permitted by SUP only.

## Slide 5: Supplemental regulations – overview and max. acreage
The Committee is also developing a new Article 28, supplemental regulations to regulate the siting, construction, management and decommissioning of utility-scale solar generation facilities (USSGFs).
The maximum size for any USSGF is 500 acres, and no more than three percent of total County acreage (approx. 5400 acres) may be used for USSGFs and no more than one (1) percent of the total County acreage within each election district (approximately 1800 acres) may be used for USSGFs.

## Slide 6: Acreage by District
District | Total Acreage | 1% of Total Acreage (*) | Percentage that is 1,800 acres (*)
Columbia | 66,458.732 ac. | 664.59 ac. | 2.7%
Cunningham | 31,234.876 ac. | 312.35 ac. | 5.76%
Fork Union | 71,817.875 ac. | 718.18 ac. | 2.5%
Palmyra | 15,048.296 ac. | 150.48 ac. | 11.96%
Rivanna | 1,843.911 ac. | 18.44 ac. | 97.62%
* Numbers rounded

## Slide 7: Supplemental regulations - Setbacks
500 feet from dwellings on the adjacent parcels.
375 feet from the adjacent property lines.
300 feet from all public right-of-way.
500 feet from entrance corridors which include Route 6, US 15, Route 53, and US 250.
1,000 feet from the James, Rivanna, and Hardware Rivers, and all lakes.
500 feet from ponds and perennial streams.

## Slide 8: Supplemental regulations – buffers and screening
USSGFs must be screened from ground-level view by a vegetative buffer of at least 175 feet, located within the required setback and around the entire perimeter.
The owner/developer may use an existing forest buffer, new vegetative screening, or berms.
Performance bonds will be posted to ensure maintenance of vegetative buffers, to be released only after decommissioning.

## Slide 9: Supplemental regulations – height, fencing, lighting, glare
Maximum structure height will be 20 feet above ground.
USSGF project area must be enclosed by six-foot high security fencing with opaque screening on the interior of the vegetative buffer, while allowing access corridors for wildlife.
Outdoor lighting will be permitted only for security and on-sight maintenance, and shall be shielded and dark sky compliant.
Solar panels will be placed to prevent concentrated radiation or glare being directed onto other properties or roads.

## Slide 10: Supplemental regulations – signs, emergency access, noise
Except for signs with emergency information at each access point, no signage will be allowed on the fencing, structures or buildings in the USSGF project area.
Emergency access will be provided in at least two separate access points.
Emergency Access 20’ looping road around interior of fence but outside panel area
Construction activity is limited to 7:00 a.m. – 6:00 p.m. on Monday through Saturday, other than emergency repairs.

## Slide 11: Supplemental regulations – wiring and transmission lines
Wiring and all new distribution and transmission lines will be underground.
New transmission lines will be subject to plan of development review.
Wires located on the poles of solar panels will be in conduit.

## Slide 12: Wildlife corridors
If the project area is larger than 50 acres, the application must identify wildlife corridors that are shown on the site plan.
Areas between fencing shall be kept open to allow for movement of migratory animals and other wildlife.

## Slide 13: Supplemental regulations – landscaping plan
A landscaping plan will be required with the SUP application, which will:
  Maximize preservation of existing trees and vegetation.
  Include tree inventory.
  Existing plant material must consist of a mix of evergreen and deciduous trees.
  For new vegetative buffer, native and pollinator-friendly plant species are preferred.
    The evergreens must have a minimum planting height of eight feet.
    Deciduous trees must have a minimum 2 inch caliper.
  All landscaping shown on the approved plan shall be installed prior to beginning power production.

## Slide 14: Supplemental regulations – vegetation management, E&S
Vegetation management plan
  Description of ground cover, plan for management.
  Only biodegradable soap and water may be used to clean surface of solar panels.
Erosion & sediment control plan
  Must be approved by Soil and Water Conservation District and DEQ prior to land disturbance.
  No topsoil may be removed from the site, but must be used onsite.
  Applicant may be required to fund a third-party E&S control inspector during construction, to be chosen by County Planning Director.

## Slide 15: Supplemental regulations – slopes, historic resources
Panels shall not be installed on steep slopes of 20% or greater; such slopes must remain undisturbed to the maximum extent practicable.
Impact analysis is required for historical and cultural resources, including grave sites. If any such resources are identified, analysis shall include a proposed plan to preserve and protect them through avoidance, minimization or mitigation.

## Slide 16: Supplemental regulations – groundwater, emergency response
Groundwater monitoring must take place before construction, upon completion of construction, every five years during the operation of the USSGF, and upon completion of decommissioning. Results must be provided to County Planning Director.
Before completion of construction, the facility owner or operator must provide the County Planning Director with an emergency management plan for all phases of the life of the facility.
Emergency personnel must be provided a knox box or code to access the property.
Owner/operator must coordinate plans and training with Fluvanna Fire and Rescue.

## Slide 17: Supplemental regulations – decommissioning
Draft decommissioning and reclamation plan must be submitted and approved before permit issuance.
Decommissioning plans to be updated every five years.
USSGFs that have not been in active and continuous service for a period of six months must be removed at the expense of the owner or operator.
Surety agreement in the full amount of estimated decommissioning costs must be submitted before a building or land disturbing permit is issued.
Panels must be recycled at a certified recycling facility.

## Slide 18: Supplemental Regulations – Review of USSGFs
The County may engage independent third-party consultants to review special use permit applications and associated documents for completeness and compliance with applicable County, state and federal laws. Any costs associated with the review shall be paid by the applicant.
In issuing any special use permit for a USSGF, the Board of Supervisors may waive or modify any of the requirements of this article.
The property will be subject to inspection by County officers and employees upon reasonable notice to the owner/operator of the USSGF.

## Slide 19: ZTA 24:04
Public Hearing (with 5 minutes per speaker)

## Slide 20: ZTA 24:04
Planning Commissioners Discussion

## Slide 21: Planning Commission Recommendation
I move that the Planning Commission recommends (approval / denial / deferral) of ZTA 24:04, an ordinance to amend and reordain the Code of the County of Fluvanna, Virginia by amending §22-2-1, Enacting §§22-3-1 through 22-3-5.4 and Enacting §22-28-1 through 22-28-25 to create a Solar Zoning District and to add supplemental regulations for utility scale solar generation facilities.